## Slide 1
HL-Pow: A Learning-Based Power Modeling Framework for High-Level Synthesis
Zhe Lin1, Jieru Zhao1, Sharad Sinha2, Wei Zhang1
1Hong Kong University of Science and Technology (HKUST)
2Indian Institute of Technology (IIT) Goa

## Slide 2
Outline
Introduction
Related Work
Power Modeling Framework
Design Space Exploration
Conclusion

## Slide 3
Outline
Introduction
Related Work
Power Modeling Framework
Design Space Exploration
Conclusion

## Slide 4
FPGA Overview
Field-Programmable Gate Array (FPGA)
  Customizable logic blocks and wirings
  On-chip memory and arithmetic units

## Slide 5
High-Level Synthesis (HLS)
C/C++ → hardware description languages
  Front-end
  Intermediate representation (IR) generation
  Bitwidth reduction, loop unrolling, etc
Back-end
  Resource allocation, scheduling, binding
  Register-transfer level (RTL) code generation
Directives to tune latency/resource
  Loop unrolling: duplicate loop copies
  Loop pipelining: pipeline stages
  Array partitioning: split memories

## Slide 6
FPGA Power Issue
  A key design constraint
  Single FPGA: increase with size and density; heterogeneous systems
  Multiple FPGAs: large-scale applications / datacenters

## Slide 7
FPGA Power Evaluation
  Go through synthesis, placement and routing → a long time
  Estimation: gate-level power analysis
  Measurement: onboard measurement
  Design-time power analysis:
    Trade off between performance / resource / power
    → Large run-time overheads
RTL design
Logic synthesis
Placement
Routing
Gate-level netlist
Bitstream
Power estimation
Power measurement

## Slide 8
Contributions
  HL-Pow framework: Fast and early-stage power estimation
  DSE framework: Power-oriented design space exploration (DSE)

## Slide 9
Outline
Introduction
Related Work
Power Modeling Framework
Design Space Exploration
Conclusion

## Slide 10
Low-Level Power Modeling
Component-based power characterization
  Power library: input-power mapping per component [shao et al, 2014]
  Consider variations in bitwidths/cell selection, etc
  Aggregation of component power for design power

## Slide 11
High-Level Power Modeling
Tile-based power modeling
    Target: affine functions [Zuo et al, 2015]
    Decompose the functions into tiles
    Power characterization for tiles

## Slide 12
High-Level Power Modeling
Phase-based power modeling
    Target: OpenCL
    Work groups & work items in OpenCL [Liang et al, 2018]
    Power phases in groups/items

## Slide 13
Motivation
Problems of power modeling works
  Long time for power characterization
  Require hardware expertise
  Dedicate to specific code structures/applications
Pre-RTL power modeling
High accuracy
High efficiency
High generalization ability

## Slide 14
Outline
Introduction
Related Work
Power Modeling Framework
Design Space Exploration
Conclusion

## Slide 15
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS

## Slide 16
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS
    Feature construction

## Slide 17
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS
    Feature construction
    RTL implementation
    Collect ground truth power values

## Slide 18
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS
    Feature construction
    RTL implementation
    Collect ground truth power values
    Power model training

## Slide 19
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS
    Feature construction
    RTL implementation
    Collect ground truth power values
    Power model training
    Prediction phase
    Pass through HLS

## Slide 20
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS
    Feature construction
    RTL implementation
    Collect ground truth power values
    Power model training
    Prediction phase
    Pass through HLS
    Feature construction

## Slide 21
Overall Design Flow
Training phase
    Collect training applications
    Pass through HLS
    Feature construction
    RTL implementation
    Collect ground truth power values
    Power model training
    Prediction phase
    Pass through HLS
    Feature construction
    Power inference

## Slide 22
Data Collection
FPGA power decomposition
  Static power: leakage power when the design is powered up, related to the scale of the design
  Dynamic power: proportional to signal activity, capacitance, voltage and frequency
  Data files collected from HLS for each design point
    Overall design: HLS report (xxx.verbose.rpt.xml), IR code (a.o.3.bc)
    Individual operator: IR operator information (xxx.adb), RTL operator information (xxx.adb.xml)

## Slide 23
Feature Construction: Architecture Features
Resource Utilization
  Look-up table (LUT)
  Digital signal processing (DSP)
  Flip-flop (FF)
  Block random access memory (BRAM)
  Performance
    Latency in cycles
    Frequency in nano-seconds
  Scaling factors of metrics
    Baseline design: the design point without any optimization
    Normalize across different applications

## Slide 24
Feature Construction: Activity Features
Conduct in high-level instead of gate-level
IR annotator: add activity tracking functions in IR
Activity generator: collect cycle-level activities
Histogram constructor: construct activity features
IR code
IR op info
RTL op info
Testbench
Act track func lib
Activity generator
Histogram constructor
IR annotator
Activity features

## Slide 25
Activity Features: IR Annotator
Instrument the IR code with activity tracking functions for each RTL operator
IR operator: in IR code
RTL operator: in hardware
RTL-to-IR back tracing
    Multiple IR ops one RTL op
    Match IR ops to RTL ops by netlist name

## Slide 26
Activity Features: IR Annotator
Instrument the IR code with activity tracking functions for each RTL operator
IR operator: in IR code
RTL operator: in hardware
RTL-to-IR back tracing
  Multiple IR ops one RTL op
  Match IR ops to RTL ops by netlist name
  Activity tracking
    Add activity tacking functions
    Record cycle-level input/output + RTL op ID
    Generate an annotated IR code

## Slide 27
Activity Features: Activity Generator
Compute average activities of each RTL operator
  Compile into link files (.o)
  Combine, compile into executable
  Run with input vectors
  Create an activity table per RTL op

## Slide 28
Activity Features: Activity Generator
  Hamming distance: count differences bit by bit
  Average the activity per RTL op
  Amortize the activities over the total execution
Hamming distance
Avg. across cycles & operands
Op exe cycles / latency

## Slide 29
Activity Features: Histogram Constructor
Operator activities → features
Fix the size of the feature set
Use a histogram representation
Allocate a histogram per opcode
Features per bin: #ops, percentage, average activity
+
+
+
+1
+1
SA: 1.5
SA: 2.2
0
2
4
6
8
10
# ops
percentage
avg. activity
Per-bin information

## Slide 30
Power Modeling
256 features: 11 architecture features, 245 activity features
Ground truth power values through onboard measurement
Regression models
  Linear regression: classic linear model, LASSO
  Support vector machine (SVM): RBF kernel
  Tree-based model: decision tree, ensemble model
  Neural network: CNN, ResNet
Data normalization
Feature selection
Cross validation
16
16
Architecture features
Activity features
16-by-16 mesh
Data normalization
Based on widely used instances

## Slide 31
Experimental Results
    Experimental setup
      Training: 15 applications / 8784 design points
      Testing: 6 applications / 2542 design points (> 20%)
    Accuracy of power modeling
      Show the best instance per type
      Linear/SVM: ~10% test error
      CNN: 4.67% test error

## Slide 32
Outline
Introduction
Related Work
Power Modeling Framework
Design Space Exploration
Conclusion

## Slide 33
Design Space Exploration (DSE)
Latency: by HLS
Power: by our power modeling flow (HL-Pow)
Trade off between latency and power
  Brute-force DSE: HLS run-time overheads
  To speed up DSE: design point sampling

## Slide 34
Design Space Exploration (DSE)
1. Design space pruning & division
  Remove repetitive design points
  Pipeline outer loop = unroll inner loops
  Divide design space by partitioning factor
  2. Initial sampling
    Collect the first set of design points to assess
    Power trend
      Pipeline outer loop > pipeline inner loop > no pipeline
      Large unrolling factor > small unrolling factor
    Grid representation of unroll/pipeline
    Select boundary and middle points

## Slide 35
Design Space Exploration (DSE)
3. Design evaluation
  Use HLS for latency evaluation
  Use HL-Pow for fast power evaluation
  4. Pareto frontier search
    Approximate Pareto frontier from sampling points
    Trade off between latency and power

## Slide 36
Design Space Exploration (DSE)
  5. Candidate selection
    Standard deviation reduction (SDR): the higher SDR, the larger impact
    SDR: pipeline > unroll → latency/power impact: pipeline > unroll
    Order sequence: first pipeline, second unroll
    Select middle points of two pareto-optimal points

## Slide 37
Design Space Exploration (DSE)
  Algorithm decomposition
    1. Design space pruning & division
    2. Initial sampling
    3. Design evaluation
    4. Pareto frontier search
    5. Candidate selection
iterate

## Slide 38
Experimental Results
    Design space exploration
      Metric: average distance to reference set (ADRS), to see how close two Pareto set is
      Initial sampling rates: different rates converge, but a small rate benefits small sampling budgets
      Total sampling budgets:
        20%: ADRS = 2.35%
        40%: ADRS = 1.84%
      ADRS decreases rapidly as the sampling budget increases from the start
Initial sampling rates
Sampling budgets
Initial sampling rate = 2%
Sampling budget = 20%

## Slide 39
Outline
Introduction
Related Work
Power Modeling Framework
Design Space Exploration
Conclusion

## Slide 40
Conclusion
    HL-Pow: HLS power modeling
      Early-stage
      Accurate
      Fast
      High generalization ability
    Power-oriented DSE
    Characteristics of HLS directives
    Trim down design space
    Iterative search flow

## Slide 41
THANK YOU
Q & A

## Slide 42
Operator type

## Slide 43
Directive

## Slide 44
ADRS