## Slide 1
Machine Learning Based Routing Congestion Prediction in FPGA High-Level Synthesis
Jieru Zhao1, Tingyuan Liang1, Sharad Sinha2, Wei Zhang1
1Hong Kong University of Science and Technology (HKUST)
2Indian Institute of Technology Goa (IIT Goa)
IIT GOA
INDIAN INSTITUTE OF TECHNOLOGY GOA

## Slide 2
Background
Machine-Learning Based Methodology
Experimental Results
Conclusion
Outline

## Slide 3
Background
Machine-Learning Based Methodology
Experimental Results
Conclusion
Outline

## Slide 4
Background: FPGA
Basic FPGA Architecture:
LUT
Flip-flop
DSP Block
Storage elements: BRAM
As an accelerator, FPGA has:
High performance
Low power
Programmability & Flexibility
Short time-to-market
A wide range of applications:
Data center
Image processing
Communications
…

## Slide 5
FPGA CAD design flow
BitStream
HDL
Frontend Compilation
IR
Scheduling
C/C++
Hardware Binding
Code Generation
Logic Synthesis
Technology Mapping
Place and Route (PAR)
Netlist
[Source from Xilinx]
RTL Implementation Flow
Error-prone and time-consuming.
High performance.
Hard to debug.
High development cost.

## Slide 6
FPGA CAD design flow
Frontend Compilation
IR
Scheduling
C/C++
Hardware Binding
Code Generation
High-Level Synthesis Flow
Easier to implement.
Hard to grasp hardware implementation details.
Fast design space exploration.
BitStream
HDL
Logic Synthesis
Technology Mapping
Place and Route (PAR)
Netlist
[Source from Xilinx]
RTL Implementation Flow
Error-prone and time-consuming.
High performance.
Hard to debug.
High development cost.

## Slide 7
In FPGA design, routing contributes a lot to delay and resource utilization.
Issue: Routing Congestion
Netlist
Placement
Routing
BitStream
HDL
Logic Synthesis
Technology Mapping
Place and Route (PAR)
Netlist
Congested region
Wires are detoured
Longer delays
More routing resources
Degrade performance
Implementation failures

## Slide 8
Physical design: Routability driven placement.
  Time-consuming: invoke the router repeatedly.
  Congestion prediction model guides the placement.
  Machine learning techniques.
  Features: #bounding boxes, half-perimeter wirelength (HPWL), #pins …
When the abstraction level increases…
  Beneficial: easier to resolve congestion at C source-code level.
  Time-consuming: run the C-to-bitstream flow.
  Congestion prediction is required.
How to solve this issue?
Question: How to predict routing congestion in HLS?

## Slide 9
Lack of physical metrics or features at a higher level of abstraction.
  Physical features obtained during placement: #bounding boxes, HPWL, #pins …
Challenges
Extract new informative features in HLS.
GUI-based “back to verilog” for each CLB after PAR.
  Not applicable to build a dataset containing a large number of samples.
  We need “back to C”.
Choice of machine learning models.
  Linear, ANN, Decision tree…
Automate the process: congestion metrics per CLB -> operations in C code.
Explore different kinds of machine learning models.

## Slide 10
Motivational Example
Synthesis directives are applied to configure the design.
  Loop unrolling
  Loop pipelining
  Array partitioning
  Function inlining
  …
Hardware-friendly C code.
Careful selection of directives.
For HLS-based designs,
Applications are implemented with C/C++.

## Slide 11
Motivational Example
Implementation | WNS (ns) | Max Freq. (MHz) | Latency (cycles) | Max Congestion (%)
With directives | -13.643 | 42.3 | 1.08 × 106 | 178.96
Without directives | -0.066 | 99.3 | 1.73 × 107 | 58.51
Application: Face Detection.
Note: WNS denotes the worst negative slack.
By applying several directives as shown in the application code:
Latency (cycles)
Congestion
Max frequency
Routing Congestion Maps.
By early detection, we can avoid non-friendly coding style and improper directives!
Time cost:
Logic synthesis and PAR: nearly 7 hours.
HLS: several minutes.

## Slide 12
To the best of our knowledge, we are the first to build a routing congestion prediction model in FPGA HLS.
We develop an automatic tool to back trace the congestion metrics of CLBs and link with the HLS IR.
We propose seven informative categories of features and compare three machine learning models.
We propose effective solutions to resolve routing congestion.
Our Contributions

## Slide 13
Background
Machine-Learning Based Methodology
Experimental Results
Conclusion
Outline

## Slide 14
Overview of our approach
High Level Synthesis Flow
Congestion
metrics
IR
HDL
C/C++
RTL Implementation Flow
Model Training
Information Collection
Back Tracing
Feature
Extraction
Dataset
Models
Congested
Region
High Level Synthesis Flow
Modified Design
Features
Congestion Resolving
Design
Model Training
Congestion
Prediction
Training Phase
Construct the dataset for training.
  Back tracing
  Information collection
  Feature extraction
Model training
Prediction Phase
Congestion prediction
Congestion resolving
Optimized Design

## Slide 15
1. Automatic Back Tracing
Congestion metrics
HDL
Frontend Compilation
IR
Scheduling
C/C++
Hardware Binding
Code Generation
Logic Synthesis
Technology Mapping
Place and Route (PAR)
Netlist
Intermediate Representation (IR)
id=“1858”:
%II_V_5_10_1 = phi i18 [ 0, %... ], [ %p_II_135_V, %...]
……
id=“3373”:
%tmp_35_5_s = sext i14 %r_V_4_5_s to i18
id=“3374”:
%p_II_135_V = add i18 %tmp_35_5_s, %II_V_5_1
CLB, Row, Column, Vertical Cong(%), Horizontal Cong(%)
CLBLM_R_X71Y149, 7, 129, 36.02, 48.33
CLBLM_R_X69Y52, 101, 172, 87.05, 39.04
…….
CLB, Net of the output Pin
CLBLM_R_X69Y98, p_II_112_V_reg_58246[7]_i_7_n_4
CLBLM_R_X69Y52, SI_V_24_35_1_reg_30030_reg_r_
…….
HDL Description
assign p_II_135_V_fu =
($signed(tmp_35_5_s_fu) + $signed(II_V_5_10_1_reg));
……
assign p_II_112_V_fu =
($signed(tmp_35_4_11_fu) + $signed(II_V_4_12_1_reg));
Source Code
for ( u = 0; u < window_size; u++)
#pragma HLS unroll
for ( v = 0; v < window_size; v++ )
#pragma HLS unroll
II[u][v] = II[u][v] + ( I[u][v+1] - I[u][0] );
High-Level Synthesis Flow
RTL Implementation Flow
RTL operations in HDL description.
Net of the output pin for each CLB.
Congestion metrics and corresponding CLB coordinates.
IR operations in LLVM IR.
C statements in the source code.

## Slide 16
2. Information Collection
Each sample in the dataset contains:
Features of each operation.
Labels: corresponding congestion metrics.
To extract features, a graph is constructed to store the HLS-based information.
Node: HLS IR operations.
Node attributes: resource usage, bitwidth, delay…
Edge: dependency among operations.
Edge weight: the number of wires for the corresponding connection.
Resource sharing: merge the nodes that share the RTL module.
Function Interface: add I/O port in the graph.
When constructing the graph, we also consider…
1
3
2
b
d
1
3
2
c
a

## Slide 17
3. Features
Category | Feature Descriptions
Bitwidth | Bitwidth of each operation.
Inter-connection | Fan-in and fan-out of each operator and their summation; #predecessors, #successors and the summation; The max. number of wires among all the connections to one-hop neighbors and its percentage of the total fan-in and fan-out. Corresponding features after including two-hop neighbors.
Resource (for each type) | Resource usage and utilization ratios of each operation; The total resource usage and utilization ratios of all the predecessors, successors and their summation; The max. resource usage and corresponding percentage among all the one-hop neighbors; Corresponding features after include two-hop neighbors.
Timing | Delay(ns) and latency(clock cycles) of each operation.
 | Resource usage and utilization ratios of predecessors/successors, divided by the subtraction of control states ; Corresponding features for two-hop neighbors.
Operator Type | The operation type of each operator; The number of each kind of operations among one-hop neighbors.
Global Information | Resource usage of the top-level function (), the function in which the operation is located () and the corresponding percentage of the resources of ; Target/estimated clock period and clock uncertainty of and ; Memories: #words, #banks, #bits and #primitives(words*bits*banks); Multiplexers: number, resource usage, input size and bitwidth.
Category | Feature Descriptions
Bitwidth | Bitwidth of each operation.
Inter-connection | Fan-in and fan-out of each operator and their summation; #predecessors, #successors and the summation; The max. number of wires among all the connections to one-hop neighbors and its percentage of the total fan-in and fan-out. Corresponding features after including two-hop neighbors.
Resource (for each type) | Resource usage and utilization ratios of each operation; The total resource usage and utilization ratios of all the predecessors, successors and their summation; The max. resource usage and corresponding percentage among all the one-hop neighbors; Corresponding features after include two-hop neighbors.
Timing | Delay(ns) and latency(clock cycles) of each operation.
Operator Type | The operation type of each operator; The number of each kind of operations among one-hop neighbors.
Global Information | 
Notes: Brief introduction

## Slide 18
3. Features
In summary, for each operator, we consider:
Features of the operator itself.
  Bitwidth, fan-in, fan-out, timing-related features, resource usage…
Features that reflect the global information.
  Total resource usage of the functions, target/estimated clock period, #mux…
Features that reflect the impact of neighboring operators.
  One-hop neighbors.
  Two-hop neighbors.
Notes: Summarize

## Slide 19
3. Features
Neighboring operators:
1
1
2
0
1
2
1
2
2
2
3
4
1
1
2
0
1
2
1
2
2
2
3
4
  One-hop neighbors
  Two-hop neighbors
Inter-connections
Resource usage
Spatial distance
Features that reflect the impact of neighbors:
a
C=1
C=2
C=3
C=4
and are two successors of operator a.
: execute immediately after a;
: execute several cycles later.
The distance constraints between a and, are different.
For , = 1.
For , = 3.

## Slide 20
4. Model Training
Sample filtering: filter outliers and improve the quality of the dataset.
Distribution of the vertical routing congestion metrics for Face Detection on FPGA.
Unroll a loop with a large unrolling factor.
Multiple copies of the same operation.
These copies can be placed to distant locations.
Some are placed around the margin of FPGA.
Their congestion metrics deviate from most of the replicas (~3% outliers).

## Slide 21
4. Model Training
Machine learning models: compare and select the best model for our problem.
Lasso linear model.
  Linear relationships.
  Tuning parameter: the constant α that multiplies the L1-norm.
Artificial neural network (ANN).
  Several hidden layers between the input and output layers.
  Tuning parameter: a number of hyperparameters.
Gradient boosted regression trees (GBRT)
  Multiple weak prediction models are combined to form a powerful regression ensemble.
  Tuning parameter: the number of estimators, the learning rate…

## Slide 22
5. Congestion Prediction
Models
Congested
Region
High Level Synthesis Flow
Modified Design
Features
Congestion Resolving
Design
Congestion
Prediction
Model training
Optimized Design
Based on the trained model, the congested regions can be detected in the C/C++ source code.
Analyze the reasons of the routing congestion and find solutions.
  Modify source code.
  Change synthesis directives.
Recursively mitigate congestion and optimize the target application.
Case Study

## Slide 23
Background
Machine-Learning Based Methodology
Experimental Results
Conclusion
Outline

## Slide 24
Benchmark suite: Rosetta.
Device: Xilinx FPGA xc7z020clg484.
Our dataset contains 8111 samples.
302 features in seven categories.
3 labels: vertical congestion metric, horizontal congestion metric and their average.
Tools: Vivado design suite 2018.1, Scikit-learn machine learning library.
The property of the benchmarks are shown in:
Experiments
Congestion Metrics | WNS (ns) | Frequency (MHz) | Vertical Congestion (%) | Horizontal Congestion (%) | Avg. (V, H) Congestion (%)
Max | -3.253 | 75.5 | 133.33 | 178.96 | 144.87
Min | -13.643 | 42.3 | 5.06 | 8.90 | 6.73
Avg. | -8.386 | 54.4 | 60.58 | 72.47 | 64.89

## Slide 25
Estimation Accuracy
Regression Models |  | Vertical Congestion (%) |  | Horizontal Congestion (%) |  | Avg. (V, H) Congestion (%) | 
 |  | MAE | MedAE | MAE | MedAE | MAE | MedAE
Not Filtering | Linear | 13.90 | 10.88 | 18.02 | 12.62 | 13.73 | 9.94
 | ANN | 12.19 | 7.91 | 17.68 | 12.62 | 12.27 | 8.17
 | GBRT | 10.55 | 7.37 | 15.71 | 10.89 | 10.57 | 6.78
Filtering | Linear | 12.41 | 9.20 | 17.48 | 12.16 | 12.76 | 9.50
 | ANN | 10.23 | 7.43 | 16.61 | 11.78 | 11.67 | 7.83
 | GBRT | 9.59 | 6.71 | 14.54 | 10.05 | 9.70 | 6.81
10-fold cross validation and grid search.
Mean absolute error (MAE) measures the average value of the absolute relative errors.
Median absolute error (MedAE) reflects the distribution of the absolute relative errors.
Best performance: the GBRT model.

## Slide 26
Congestion Metrics | Vertical Congestion | Horizontal Congestion | Avg. (V, H) Congestion
Important Feature Categories |  |  | Resource
 | Resource | Resource | 
 | Interconnection | Interconnection | Interconnection
 | Global (Mux) | Global (Memory) | Global (Mux)
Congestion Metrics | Vertical Congestion | Horizontal Congestion | Avg. (V, H) Congestion
Important Feature Categories |  |  | Resource
 | Resource | Resource | 
 | Interconnection | Interconnection | Interconnection
 | Global (Mux) | Global (Memory) | Global (Mux)
Important Features
Importance of different categories of features is assessed through the GBRT model.
has the greatest impact on both vertical and horizontal congestion metrics.
The related information of multiplexers and memories has a greater effect than other global features.
Importance rank

## Slide 27
Case Study
Implementation | WNS (ns) | Max Freq. (MHz) | Latency (cycles) | Max Congestion Vert, Hori (%) | #Congested CLBs (>= 100%)
Baseline | -13.643 | 42.3 | 1.08 × 106 | 133.33, 178.96 | 1272
Implementation | WNS (ns) | Max Freq. (MHz) |  | Max Congestion Vert, Hori (%) | #Congested CLBs (>= 100%)
Baseline | -13.643 | 42.3 | 1.08 × 106 | 133.33, 178.96 | 1272
Application: Face Detection
Baseline: Original design.
Severe routing congestion degrades the maximum frequency significantly.
Performance trade-off
Baseline(H)
Baseline(V)

## Slide 28
Case Study
Implementation | WNS (ns) | Max Freq. (MHz) | Latency (cycles) | Max Congestion Vert, Hori (%) | #Congested CLBs (>= 100%)
Baseline | -13.643 | 42.3 | 1.08 × 106 | 133.33, 178.96 | 1272
Not Inline | -3.504 | 74.1 | +23 | 129.85, 97.60 | 193
Implementation | WNS (ns) | Max Freq. (MHz) |  | Max Congestion Vert, Hori (%) | #Congested CLBs (>= 100%)
Baseline | -13.643 | 42.3 | 1.08 × 106 | 133.33, 178.96 | 1272
Not Inline | -3.504 | 74.1 | +23 | 129.85, 97.60 | 193
Step 1
Not Inline(V)
Step 1
Not Inline(H)
Baseline(H)
Baseline(V)
Step 1: Not Inline
The classification function contains 52 classifiers.
Function inlining increases the complexity in C synthesis and generates a larger design.
Not inline the classifiers.

## Slide 29
Case Study
Implementation | WNS (ns) | Max Freq. (MHz) | Latency (cycles) | Max Congestion Vert, Hori (%) | #Congested CLBs (>= 100%)
Baseline | -13.643 | 42.3 | 1.08 × 106 | 133.33, 178.96 | 1272
Not Inline | -3.504 | 74.1 | +23 | 129.85, 97.60 | 193
Replication | -0.767 | 92.9 | +0 | 106.15, 104.73 | 17
Implementation | WNS (ns) | Max Freq. (MHz) |  | Max Congestion Vert, Hori (%) | #Congested CLBs (>= 100%)
Baseline | -13.643 | 42.3 | 1.08 × 106 | 133.33, 178.96 | 1272
Not Inline | -3.504 | 74.1 | +23 | 129.85, 97.60 | 193
Replication | -0.767 | 92.9 | +0 | 106.15, 104.73 | 17
Step 1
Not Inline(V)
Step 1
Not Inline(H)
Step 2
Replication(H)
Step 2
Replication(V)
Baseline(H)
Baseline(V)
Step 2: Replication
All the classifiers access the same completely partitioned array and multiple classifiers share the same inputs.
A large number of interconnections.
Modify the source code by replicating the values of the input data and sending copies to different classifiers.

## Slide 30
Background
Machine-Learning Based Methodology
Experimental Results
Conclusion
Outline

## Slide 31
We propose a novel machine-learning based methodology to predict routing congestion in FPGA HLS.
Experiments show that the GBRT model achieves the highest prediction accuracy.
Based on our model, routing congestion can be mitigated step by step and the performance of Face Detection can be improved significantly.
Conclusion

## Slide 32
Thank you for listening!
Q & A