## Slide 1: COMBA: A Comprehensive Model-Based Analysis Framework for High Level Synthesis of Real Applications
Jieru Zhao | Hong Kong Univ. of Science and Technology
Liang Feng | Hong Kong Univ. of Science and Technology
Sharad Sinha | Nanyang Technological Univ., Singapore
Wei Zhang | Hong Kong Univ. of Science and Technology
Yun Liang | Peking Univ., China
Bingsheng He | National Univ. of Singapore

## Slide 2: Why FPGA?
High performance
Low power
Post-fabrication reconfigurability
Short time-to-market
Background

## Slide 3: FPGA Applications
Wired Communications
Data Center
Medical
Wireless Communications
Broadcast
Aerospace and Defense
Automotive
Background

## Slide 4: High Level Synthesis
HLS
Allocation
Scheduling
Hardware Binding
Programmability of FPGA is further improved!
Behavioral Description
(C/C++/SystemC)
Hardware Description
(Verilog/VHDL)
Automatic Transformation

## Slide 5: Pragmas in HLS tool
Selection of directives/pragmas
Directives in Vivado HLS
Function
Loop
Array
Dataflow
Function Pipelining
Function Inlining
Loop Unrolling
Loop Pipelining
Loop Flattening
Array Partitioning
Block
Cyclic
Complete
The quality of RTL designs
Determines
How to choose the most suitable pragmas quickly?

## Slide 6: Motivational Example
The performance difference can be very large!
~30x
~40x
More than millions of combinations.
Important:
To choose the best configuration.
Difficult:
To quickly find the best one.
For this application, COMBA spends 10 min to find the high-performance configuration, in a design space with 7.61 × 1012 points.

## Slide 7: Contributions
State-of-the-art
Three pragmas
Performance models for simple code structures
No resource models
Small design space: ~102 points
Design space exploration:
Brute force method
COMBA
Seven pragmas
Performance models for more complex code structures
Resource models: DSP and BRAM
Enlarged design space: ~108 points
Design space exploration:
Efficient Metric-Guided DSE algorithm

## Slide 8: Overview
Optimal Configuration
RDC
Library
Pragmas
Performance Model
Resource Model
MGDSE
Redundancy
Elimination
C/C++ Source Code
Model
Frequency
Operation Chaining
DFG Construction
Guided
Search
Clang Front End
RDC: Recursive data collector.
Computes the parameters required by our model.
Model: Estimates the performance and resource usage
MGDSE: an algorithm for design space exploration
Evaluates the estimated results
Sets the next configuration for RDC.
COMBA iterates until it finds the high-performance configuration.
Framework
  RDC
  Models
  MGDSE
Background

## Slide 9: Recursive Data Collection
RDC: an optimization pass based on llvm::Module class.
LLVM IR: LLVM intermediate representation
Library
Pragmas
Parameters
Frequency
Operation Chaining
DFG Construction
LLVM IR
void function(…)
{
  int a = t * m;
  int c = a + b;
  sub_func1(a, *p);
  sub_func2(c, *q);
  loop1{
  p[i] …
  }
  loop2{
  q[i] …
  }
}
a
c
sub1
sub2
loop1
loop2
Logic operations
Loops
Invoked functions
Library
Pragmas
Parameters
Frequency
Operation Chaining
DFG Construction
LLVM IR
More than one operation can be scheduled in one cycle if possible.
➊
Data flow graph (DFG) construction
Operation chaining
A dynamic programming approach is employed to trace each path and compute the latency in the critical path.
Framework
  RDC
  Models
  MGDSE

## Slide 10: Analytical Models: Performance Model
1. Loop Unrolling
➌➍➎
Iteration latency:
Loop latency:
Iteration latency of
Loop latency of
Latency of copies
Latency of
➋
Framework
  RDC
  Models
  MGDSE
Notes: Various loop hierarchies,
perfect loops
non-perfect loops
multiple loops

## Slide 11: Analytical Models: Performance Model
2. Loop Pipelining
➋➌➍➎
➋
Pipeline depth
Initiation interval
Add
Load
Load
Add
Add
…
…
…
Store
Store
Store
Load
Trip count
Tc
Latency of a pipelined loop:
Latency between the beginning of two consecutive iterations
Latency of one iteration
The number of iterations

## Slide 12
Add
Load
Load
Add
Add
Store
…
…
…
…
…
Store
…
Store
= 5
= 2
= 6
stall
Load & Store operations:
access different arrays,
Store
Store
Load
Store
Load
Store
Conflict!
stall
stall
Analytical Models: Performance Model
➋
2. Loop Pipelining:
pipeline depth,
access the same array,

## Slide 13: Analytical Models: Performance Model
2. Loop Pipelining:
Resource-constrained II
Recurrence-constrained II
If the loop contains sub-functions,
➋
initiation interval,
Add
Load
…
Store
Load
Add
Load
…
Store
Load
①
②
Add
Load
Sub
Store
Add
Load
Sub
Store
①
②
t
t
t
t
t

## Slide 14: Analytical Models: Performance Model
2. Loop Pipelining:
Perfect nested loop:
Non-perfect nested loop:
trip count,
➋
Outer loops are flattened to feed the inner loop with more data.
Codes between loop statements stop outer loops from flattening with the inner loop.

## Slide 15
Block:
Cyclic:
Complete:
Partition number in dimension
Partition number considering n-dimension array partitioning
Analytical Models: Performance Model
➋
3. Array Partitioning
Partition number shows which partition this array element is located in.

## Slide 16
resource-constrained minimum II,
the maximum function II among all sub-functions.
is the maximum II among all sub-functions and sub-loops.
“Fine-grain” pipelining: operators
“Coarse-grain” pipelining: functions and loops
Analytical Models: Performance Model
➋
4. Function Pipelining
5. Dataflow

## Slide 17
Sharable: the maximum number of parallel operators
If a loop is pipelined,
Width ratio
Depth ratio
: the number of blocks on BRAM.
#bit: the width of each array element.
e.g., int: 32 bits
#element: the number of elements in one memory partition.
width is the bandwidth of the selected block configuration.
depth is the depth of the selected block configuration.
#partition: the number of memory partitions.
: equals 2 if dataflow is applied;
equals 1 if not.
Analytical Models: Resource Model
➋
1. DSP Estimation
2. BRAM Estimation

## Slide 18
Three evaluation metrics are proposed
To remove the redundant design points based on the rules of HLS tools.
E.g., top-function: pipelined,
sub-loops: unrolled completely, cannot be pipelined.
Points related to LU, LP will be removed.
To evaluate the performance of the current design point
To determine the next design point
1. The first stage: Redundancy Elimination
2. The second stage: Guided Search
Metric-Guided Design Space Exploration
➌
Framework
  RDC
  Models
  MGDSE

## Slide 19
Three evaluation metrics:
Metric-Guided Design Space Exploration
➌
Find the bottleneck: the longest sub-function/sub-loop is assumed to have the greatest influence.
Check the resource constraints: whether the resource usage exceeds the available resources on FPGA.
Decide how to partition: which option is better, block or cyclic.

## Slide 20: MGDSE Flow
end
No pragma is set
Top function:
Dataflow
Yes
No
Producer-consumer
Function pipelining
True
False
No
Yes
end
Sub-functions: pipelined
Loops: unrolled
All arrays considered
Set array partitioning
Evaluate performance
Yes
No
Select the current longest sub-function or loop
Function
or loop?
Function
Loop
Set LU, LP
Set array partitioning
end
All cases considered
No
➊
➋
➌
Array optimization
sub-function/loop optimization

## Slide 21: Estimation Accuracy
Chart: Etimation errot (%)
| ATAX | BICG | GEMM | GESUMMV | MM | MVT | SYR2K | SYRK
Lin_analyzer | 2.68 | 1.24 | 3.25 | 5.15 | 2.69 | 2.05 | 1.32 | 2.78
COMBA | 0.71 | 0.33 | 0.46 | 1.25 | 0.83 | 0.48 | 0.47 | 0.44
 | Lin_analyzer [1] (%) | COMBA(%)
ATAX | 2.68 | 0.71
BICG | 1.24 | 0.33
GEMM | 3.25 | 0.46
GESUMMV | 5.15 | 1.25
MM | 2.69 | 0.83
MVT | 2.05 | 0.48
SYR2K | 1.32 | 0.47
SYRK | 2.78 | 0.44
Chart: Estimation error (%)
| JPEG | Seidel | Rician
COMBA | 1.54 | 0.91 | 1.12
 | COMBA (%)
JPEG | 1.54
Seidel | 0.91
Rician | 1.12
Benchmarks from Polybench
Three other applications
The estimation error is reduced!
COMBA also works for more complicated applications!
Framework
  RDC
  Models
  MGDSE
Results
[1]Lin-analyzer.: a high-level performance analysis tool for fpga-based accelerators. DAC Conference. 2016.

## Slide 22: DSE Results: Comparison
Benchmark | Design Space |  | Performance Speed-up |  | MGDSE Time (s) | 
 | Lin-analyzer[1] | COMBA | Lin-analyzer[1] | COMBA | Lin-analyzer[1] | COMBA
ATAX | 85 | 1.31 × 108 | 8.35 | 125.45 | 8.85 | 41.01
BICG | 95 | 5.76 × 108 | 15.88 | 201.38 | 22.60 | 89.20
GEMM | 85 | 1.05 × 1010 | 8.15 | 261.63 | 185.37 | 65.83
GESUMMV | 85 | 8.39 × 108 | 15.42 | 83.88 | 12.05 | 77.40
MM | 85 | 6.34 × 1013 | 15.22 | 277.03 | 161.37 | 292.15
MVT | 95 | 1.05 × 1010 | 15.30 | 189.18 | 14.88 | 57.72
SYR2K | 85 | 1.05 × 1010 | 7.27 | 123.96 | 250.01 | 223.00
SYRK | 85 | 1.64 × 108 | 8.12 | 462.65 | 168.78 | 86.34
Larger design space
Better speed-up
Efficient design space exploration
125.45
201.38
261.63
83.88
277.03
189.18
123.96
462.65
41.01
89.20
65.83
77.40
292.15
57.72
223.00
86.34
1.31 × 108
5.76 × 108
1.05 × 1010
8.39 × 108
6.34 × 1013
1.05 × 1010
1.05 × 1010
1.64 × 108
[1]Lin-analyzer.: a high-level performance analysis tool for fpga-based accelerators. DAC Conference. 2016.

## Slide 23: DSE Results: Optimizations of Polybench
For different code structures, the optimization schemes are different!

## Slide 24: Case Study: JPEG
The optimal configuration found by COMBA: “FP_AllPartition”,
which is to
pipeline the top-function,
partition the three arrays completely.
Design space: 7.61 × 1012
MGDSE time: 613s
Speed-up: 28.8x

## Slide 25: Conclusion
The proposed model-based framework, COMBA:
  Optimizes different applications with various code structures.
  Performs better than the state-of-the-art on simple benchmarks.
  Optimizes more complicated applications efficiently, within minutes.

## Slide 26
Thank you for listening!
Q & A